ARM CPU SIMULATOR
This project is the design of a single cycle (non-pipelined) processor, which is capable of performing basic arithmetic, logic and data operations. It is based on ARM 64-bit architecture, with 32 registers of 64-bits wide with instruction lengths of 32-bits each. The project is designed in such a way that the instruction memory, data memory and register memory are located outside the CPU as separate functional units and it is possible to verify each functional units separately. In the fully functional operation all the individual modules will the co-operated. The instructions needs to be stored in the instruction memory and Program Counter (PC) will be incremented by CPU with the clock. Depend on the instruction the CPU will generate corresponding control signals to control different operations and to access other modules
The assembly instructions supported by the CPU are
LDUR: Load RAM into Register
STUR: Store Register content into RAM
ADD: Add Registers
SUB: Subtract Registers
ORR: Bit-wise OR Register
AND: Bit-wise AND Register
CBZ: Conditional Jump (when the value in Register is zero)
B: Unconditional (arbitrary) Jump

The pattern of generation of machine instructions from assembly instructions is shown in the below table.
Instruction	Example	Op-code (31- 21)	READ_REG_2 / (20 to 16)	15 to 10	READ_REG_1 / (9 to 5)	WRITE_REG (4 to 0)
LDUR	LDUR r2, [r10]	1111 1000 010	0 0000	0000 00	0 1010- R10	0 0010 -R2
STUR	STUR r4, [r7]	1111 1000 010	0 0000	0000 00	0 0111 - R7	0 0100 -R4
ADD	ADD r5, r3, r2	1000 1011 000	0 0010 -R2	0000 00	0 0011 -R3	0 0101- R5
SUB	SUB r4, r3, r2	1100 1011 000	0 0010 -R2	0000 00	0 0011 -R3	0 0100 -R4
AND	AND r7, r2, r3	1000 1010 000	0 0011 -R3	0000 00	0 0010 -R2	0 0111 -R7
ORR	ORR r6, r2, r3	1010 1010 000	0 0011- R3	0000 00	0 0010 -R2	0 0110- R6
STUR	STUR r4, [r7,]	1111 1000 000	0 0000	0000 00	0 0111- R7	0 0100-R4
LDUR	LDUR r2, [r10, #1]	1111 1000 010	0 0000	0000 01	0 1010- R10	0 0010 -R2
STUR	STUR r4, [r7, #1 ]	1111 1000 000	0 0000	0000 01	0 0111 - R7	0 0100 -R4